## Slide 1: TOPOLOGICAL SIMPLIFICATION OF NESTED SHAPES
Dan Zeng, Tao Ju (Washington University in St. Louis)
Erin Chambers, David Letscher (St. Louis University)
SGP 2022

## Slide 2: Nested Shapes
A sequence of monotonically expanding shapes
Wikipedia
Notes: In this work we are interested in reconstructing a sequence of nested shapes. In such a sequence, every shape is strictly a subset of the next shape. That is, the shapes are monotonically expanding through the sequence.
Perhaps the picture that comes to your mind is the Russian dolls, which is a great example of a nested sequence.
But nested shapes can be found in nature as well

## Slide 3: Nested Shapes
Multi-layered structures
Geological strata
Tissue layers
Notes: A great example is a structure containing multiple layers, so that the inner layers are nested inside the outer layers. Such structures are found in both geology and biology.

## Slide 4: Nested Shapes
Multi-layered structures
Cerebrospinal fluid
White matter
Gray matter
Notes: Here is an example of surfaces reconstructed from 3D imaging for different layers of the brain, starting from the cerebrospinal fluid on the inside, to the white matter in the middle layer, and the gray matter on the outside.

## Slide 5: Nested Shapes
Multi-layered structures
  The outer surface of each layer forms a nested sequence
Cerebrospinal fluid
White matter
Gray matter
Notes: If we consider the outer surface of each layer, they form a nested sequence.

## Slide 6: Nested Shapes
Growing plant roots
Wikipedia
Notes: Another interesting example of nested shapes is the growing root system of a plant, such as this corn. Due to resistance of the soil, roots generally move very little in the soil, and grow mainly by becoming thicker, longer, and having more branches.

## Slide 7: Nested Shapes
Growing plant roots
Rice roots
Day 1
Day 2
Day 3
Maize (corn) roots
Day 10
Day 30
Day 40
Notes: Here I show several time series of roots reconstructed from 3D imaging. In general, that reconstructions at earlier time points are subsets of those at later time points.
While many methods are available to reconstruct these nested shapes from imaging, the resulting reconstructions typically contain errors, due to the ambiguity and noise in the raw images. The particular type of errors that we are concerned with in this work are topological errors.

## Slide 8: Topology
Invariant to continuous geometric deformation
Components
Void
Handle
Wikipedia
Notes: So what is topology? It is an aspect of a shape that does not change as the shape deforms continuously. In this animation, a coffee mug is being deformed to a donut. Obviously the geometry has changed significantly, but some aspect of the shape has not, such as the handle of the mug that turns into the donut ring.
We call features that are invariant to geometric transforms the topological features. In 3D, there are 3 types of topological features: components (which are…), voids (which are…), and handles, like the one on the coffee mug.

## Slide 9: Topology
Invariant to continuous geometric deformation
Many geometry processing tasks are sensitive to topology:
  Mesh simplification and fairing
  Surface parameterization
  Geodesic distances
  Surface matching
  Physical simulations
Mesh simplification before and after removing redundant topological features [Wood 04]
Notes: The reason that we care about topology is because they are resistant to typical geometric operations. As a result, redundant topological features may significantly affect geometric processing tasks. This picture shows the result of mesh simplification on a version of David’s head that contains many small topological handles and a version that has no handles. Clearly, simplification is much more effective at preserving the geometric shape of the model when there are no topological handles.

## Slide 10: Topological Errors
Reconstruction may introduce unwanted topological features
handles
components
Cerebrospinal fluid
White matter
Gray matter
Notes: Working with real-world data, reconstruction methods often create redundant handles, components and voids.

## Slide 11: Topological Errors
Reconstruction may introduce unwanted topological features
Day 1
Day 2
Day 3
handles
components
Notes: Here are some more examples of topological errors in a reconstructed time series of growing roots, including redundant components and handles

## Slide 12: Goal
Remove unwanted topological features in reconstructed shapes
  Maintain nesting (necessary for defining layers or modeling root growth)
Notes: The goal of our work is to remove these unwanted topological features in a given sequence of reconstructed shapes.
An important constraint is that the nesting relationship between the shapes must be maintained. Nesting is important for defining layers in a multi-layered structure, orfor computing the growth function of the root system.

## Slide 13: Previous Works
Simplifying the topology of one shape
  Removing handles [Shattuck 01; Han 02; Wood 04; Chen 06; Zhou 07; Segonne 07]
  Removing all features
    Morphological opening/closing [Nooruddin 03]
    Inflation and deflation [Kriegeskorte 01; Bischoff 02; Szymczak 03]
    Local heuristics [Ju 07]
    Global optimization [Zeng 20]
Simply connected
[Zeng 20]
Input
[Wood 04]

## Slide 14: Previous Works
Simplified:
(simply connected)
Simplifying the topology of one shape
  Cannot guarantee nesting when applied independently to each shape
Time 1
Time 2
Input:
Not nesting!

## Slide 15: Previous Works
Simplifying the topology of a scalar function
  Removes extraneous critical points, thus simplifying the topology of all level sets (which are nested)
  Numerical optimization [Bremer 04; Patane 09; Weinkauf 10; Gunther 14]
  Combinatorial methods [Edelsbrunner 06; Bauer 12; Tierny 12,17; Lukasczyk 20]
[Gunther 14]
14492 extrema
12 extrema

## Slide 16: Previous Works
Removing all local minima except one [Gunther 14]
Simplifying the topology of a scalar function
  Saddles in 3D (corresponding to handles of the level sets) are challenging to remove
handles

## Slide 17: Our Work
Simplifies the topology of a shape sequence while maintaining nesting
  Removes all three types of topological features (components, handles, voids)
  Minimally alters the shapes
Technical contributions
  Extension of the single-shape method of [Zeng 20]
  Formulation as a discrete optimization problem
  An efficient and effective solver

## Slide 18: Topological Operators
Void
Handle
Components
Filling
Cutting

## Slide 19: Single-shape Simplification [Zeng 20]

## Slide 20: Single-shape Simplification [Zeng 20]
Compute candidate cuts and fills
  Applying a cut or fill removes one or more features
  Each candidate associated with a cost
Select a subset of candidates that:
  Maximally removes topological features
  Minimizes total cost
fills
cuts

## Slide 21: Single-shape Simplification [Zeng 20]
Compute candidate cuts and fills
  Applying a cut or fill removes one or more features
  Each candidate associated with a cost
Select a subset of candidates that:
  Maximally removes topological features
  Minimizes total cost
Solved as a graph labelling problem

## Slide 22: Nesting-Aware Candidates
Cut may be used (if is also used)
Cut may never be used
Fill may be used (if is also used)
Fill may never be used
Nesting-aware

## Slide 23: Optimization Problem
Given:
  Nested shapes
  Nesting-aware candidates , each with a cost
Label candidates as inside () or outside () to:
  Maximally remove topological features of each shape
  Minimize total costs of 0-labelled cuts and 1-labelled fills
  Maintain nesting
[Zeng 20]

## Slide 24: Optimization Problem
Given:
  Nested shapes
  Nesting-aware candidates , each with a cost
Label candidates as inside () or outside () to:
  Maximally remove topological features of each shape
  Minimize total costs of 0-labelled cuts and 1-labelled fills
  Maintain nesting
cuts
fills
[Zeng 20]

## Slide 25: Optimization Problem
Given:
  Nested shapes
  Nesting-aware candidates , each with a cost
Label candidates as inside () or outside () to:
  Maximally remove topological features of each shape
  Minimize total costs of 0-labelled cuts and 1-labelled fills
  Maintain nesting
[Zeng 20]

## Slide 26: Optimization Problem
Given:
  Nested shapes
  Nesting-aware candidates , each with a cost
Label candidates as inside () or outside () to:
  Maximally remove topological features of each shape
  Minimize total costs of 0-labelled cuts and 1-labelled fills
  Avoid conflicting labels
    Conflict: overlaps with , has label 1, has label 0
[Zeng 20]

## Slide 27: Optimization Problem
Given:
  Nested shapes
  Nesting-aware candidates , each with a cost
Label candidates as inside () or outside () to:
  Maximally remove topological features of each shape
  Minimize total costs of 0-labelled cuts and 1-labelled fills
  Avoid conflicting labels
    Conflict: overlaps with , has label 1, has label 0
[Zeng 20]

## Slide 28: Solver 1: Label Propagation
Propagate labels from one shape to others while avoiding conflicts
  Use [Zeng 20] to optimize labels on each shape
overlapping
1
0
Conflict

## Slide 29: Solver 1: Label Propagation
Propagate labels from one shape to others while avoiding conflicts
  Use [Zeng 20] to optimize labels on each shape
1
0
1

## Slide 30: Solver 1: Label Propagation
Propagate labels from one shape to others while avoiding conflicts
  Use [Zeng 20] to optimize labels on each shape
1
0
1

## Slide 31: Solver 1: Label Propagation
Propagate labels from one shape to others while avoiding conflicts
  Use [Zeng 20] to optimize labels on each shape
1
0
1
1
1

## Slide 32: Solver 1: Label Propagation
Propagate labels from one shape to others while avoiding conflicts
  Use [Zeng 20] to optimize labels on each shape
1
0
1
0
1
1

## Slide 33: Solver 1: Label Propagation
Propagate labels from one shape to others while avoiding conflicts
  Use [Zeng 20] to optimize labels on each shape
1
0
1
0
1
1

## Slide 34: Solver 1: Label Propagation
Propagate labels from one shape to others while avoiding conflicts
  Use [Zeng 20] to optimize labels on each shape
1
0
1
0
1
1
0

## Slide 35: Solver 1: Label Propagation
Propagate labels from one shape to others while avoiding conflicts
  Use [Zeng 20] to optimize labels on each shape
1
0
1
0
1
1
0
1
0

## Slide 36: Solver 1: Label Propagation
Propagate labels from one shape to others while avoiding conflicts
  Among all starting shapes, take the solution with the minimal topology and costs
  Guarantees to be free of conflicts
  May not be optimal in topology simplicity or geometric cost

## Slide 37: Solver 2: State-space Search
State: a labelling of all candidates, and a set of constrained candidates
  In a queue sorted by topology + geometric cost
0
1
1
0
1
1
1
0
0
1
0
0

## Slide 38: Solver 2: State-space Search
State: a labelling of all candidates, and a set of constrained candidates
  In a queue sorted by topology + geometric cost
If the popped state has conflicts:
0
1
1
0
1
1
1
0
0
1
0
0

## Slide 39: Solver 2: State-space Search
State: a labelling of all candidates, and a set of constrained candidates
  In a queue sorted by topology + geometric cost
If the popped state has conflicts:
  Pick a conflict
  Create 2 new states by either constraining ’s label to be 0 or ’s label to be 1
0
1
1
0
1
1
1
0
0
1
0
0

## Slide 40: Solver 2: State-space Search
State: a labelling of all candidates, and a set of constrained candidates
  In a queue sorted by topology + geometric cost
If the popped state has conflicts:
  Pick a conflict
  Create 2 new states by either constraining ’s label to be 0 or ’s label to be 1
0
1
1
0
1
0
0
1
0
0

## Slide 41: Solver 2: State-space Search
State: a labelling of all candidates, and a set of constrained candidates
  In a queue sorted by topology + geometric cost
If the popped state has conflicts:
  Pick a conflict
  Create 2 new states by either constraining ’s label to be 0 or ’s label to be 1
0
0
1
0
1
0
0
1
0
0

## Slide 42: Solver 2: State-space Search
State: a labelling of all candidates, and a set of constrained candidates
  In a queue sorted by topology + geometric cost
If the popped state has conflicts:
  Pick a conflict
  Create 2 new states by either constraining ’s label to be 0 or ’s label to be 1
Terminate otherwise
0
0
1
1
0
0
1
0
0
1
0
0

## Slide 43: Solver 2: State-space Search
Best-first search in a binary tree of states
Returns optimal conflict-free labelling
  Assuming [Zeng 20] is optimal
High computational cost
  # iterations can be exponential in total # candidates

## Slide 44: Solver 3: Beam Search
Limit queue size to a constant
  Keep only best states
Trade off optimality for efficiency
  # iterations linear in total # candidates

## Slide 45: Solver Comparison
Propagation
# Level sets
Running time (secs)
Level set of
CT bone scan
# Topo. features
# Level sets
Propagation
[Zeng 20]
(not nesting)
# components: 31
# handles: 371
# voids: 106

## Slide 46: Results: Roots
Single-shape [Zeng 20]:
(Simply connected)
Time 1
Time 2
Input:
Not nesting!
Our method:
(Simply connected)

## Slide 47: Results: Roots
Day 1
Day 2
Day 3
Input:
Our method:
(Simply connected)

## Slide 48: Results: Brain
Cerebrospinal fluid
White matter
Input (nested)
Single-shape [Zeng 20]
(simply connected; not nested)
Our method
(simply connected and nested)

## Slide 49: Limitations and Future Works
Need more “natural-looking” candidates and “semantic” geometric costs
Handling non-cubical complexes
How to simplify a (not necessarily nesting) shape collection in a consistent way?
Input
Our method

## Slide 50: Acknowledgement
Dan Zeng
Danforth Plant Science Center
Chris Topp
Danforth Plant Science Center
  Chris Topp, Mao Li
Funding
  NSF ABI-1759836, NSF EF-1921728, AF-1907612 and AF-2106672
  WashU Imaging Science Pathway Fellowship (Dan)